## Slide 1: Smart HealthCare
Wearable CPS for Stress Detection
Alessia Simone
Supervisor: Prof. Maurizio Palesi
Co-Supervisor: Prof. Sebastiano Battiato

## Slide 2: Stress Disorder
Introduction
«Stress is a state of mental or emotional strain or tension resulting from adverse or demanding circumstances»
Oxford Languages
Symptoms
Cardiovascular disease
Increased sweating
Increased core temperature
Decreased peripheral temperature
Increased heart rate
Comorbidity
Anxiety
Fear

## Slide 3: What is a CPS?
Cyber
Software part
(data processing, decision-making and algorithms)
Physical
Hardware part
(sensors and actuators)
System
Cyber + Physical interconnection
Major leader of industry 4.0
They are widely used in healthcare domain where integration of wearable devices is helpful.

## Slide 4: Research Questions
Does the combination of CPS and Machine Learning produces useful results on stress detection?
What are the potential application?
Objective
Cheap and Quick CPS for stress detection

## Slide 5: WESAD Dataset
Exploratory Data Analysis
Wearable Stress and Affect Detection:
Subjects: 15 individuals
Devices: Empatica E4 and Respiban
Protocol states: neutral, stress and amusement

## Slide 7: Part 1 Methodology

## Slide 8: MobileNetV2
Deep
Learning
2M of trainable parameters
146 MB of estimated total size

## Slide 9: Gramian Angular Field Images

## Slide 10: XAI
Noise Tunnel + Guided GradCam
AVG Accuracy: 56%
Confusion Matrix

## Slide 11: 1) Features Extraction
Supervised Machine Learning
minimum
maximum
absolute minimum
absolute maximum
mean
absolute energy
mean absolute change
CID-CE

## Slide 12: 2) Hyperparameter tuning
Leave-One-Subject-Out Cross-Validation
Halving Grid Search
Weighted F1
Penalty: | Lib-Linear
Solver: | L1
C: | 1
Logistic Regression
Estimators: | 10
Max depth: | 5
Min split: | 10
Random Forest
Booster: | Tree
alpha: | 0.001
eta: | 1
lambda: | 0.001
Extreme Gradient Boosting
Variance Smoothing: | 2.31e-9
Gaussian Naive Bayes

## Slide 13: 3) Optimal Model Selection
Logistic Regression
AUC of 98% (±0.02),
F1 of 94% (±0.06),
Precision of 95% (±0.05),
Recall of 94% (±0.06),
Accuracy of 94% (±0.07)
Model Comparison
Random
Forest
Gaussian Naïve Bayes
Extreme Gradient Boosting
Logistic
Regression
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
AUC
Precision
Accuracy
F1
Recall

## Slide 14: Part 2 Deployment

## Slide 15: Hardware
Wemos D1 Mini Pro
MLX90614
MAX30101
Operating Voltage | 3.3 / 5 V
GPIO Pins | 11 (1 ADC)
Clock Speed | 80 / 160 MHz
Flash | 16 MB
Size | 34.2 * 25.6mm * 3g
Range | -70°C…+380°C for skin temperature
Resolution | 0.02°C
Accuracy | ±0.2°C within 36-38°C
Output | BVP
LED | IR, Red, Green
ADC Resolution | 18-bit
Internal Algorithm | Motion Artifact Removal, Peripheral Beat Amplitude

## Slide 16: Code Diagram Flow
Software

## Slide 18
Part 3
Experiment
Experimental procedure:
5% Recall
Stress (5 min) | Baseline (5 min)
Math quiz | Nature sounds

## Slide 19: Conclusions
Does the combination of CPS and Machine Learning produces useful results on stress detection?
What are the potential application?
Features extraction + Logistic Regression
Convolutional Neural Network
The device is highly useful during cognitive-behavioral oriented psychotherapies, to identify and correct behaviors that cause high levels of stress.
However, the mere support of the device is not sufficient for pathologies that are based on deeper and more complex psychic processes, where anxiety and stress represent surface symptoms.
Dr. Marziano A., psychologist ang psychotherapist, personal communication, 09/07/2023
Objective
Cheap: 42 €
Quick: 14 milliseconds for a response

## Slide 20: Thank you for your attention

## Slide 21: References
Batista, G. E. a. P. A., Wang, X., & Keogh, E. (2011). A Complexity-Invariant Distance Measure for Time Series. https://doi.org/10.1137/1.9781611972818.60
Cyber physical systems (CPS), cosa sono, come stanno rivoluzionando il mondo industriale | Internet4Things
Figma
Flaticon
In-Depth: Interface MLX90614 IR Temperature Sensor with Arduino
LOLIN D1 mini — WEMOS documentation
Dr. Marziano, A. (2023), psychologist and psychotherapist, personal communication about potential application of Smart Healthcare wearable CPSs.
Oxford Languages and Google - English
Quickly Compare Multiple Models. How to train and evaluate multiple… | by Cole | Towards Data Science
Sandler, M., Howard, A., Zhu, M., Zhmoginov, A., & Chen, L. (2018). MobileNetV2: Inverted Residuals and Linear Bottlenecks. arXiv. https://doi.org/10.1109/cvpr.2018.00474
Schmidt, P., Reiss, A., Duerichen, R., Marbergen, C., & Van Laerhoven, K. (2018). Introducing WESAD, a Multimodal Dataset for Wearable Stress and Affect Detection. ICMI '18: Proceedings of the 20th ACM International Conference on Multimodal Interaction, 400-408. https://doi.org/10.1145/3242969.3242985
Stress